## Slide 1
Equipment
Drawing Board, T-Square, 2H/5H
Pencil, Set-Squares & Masking tape
Step 1: Set up and line out page as per specification
Step 2: In a standard Orthographic Projection there are three planes of projection, namely the Vertical, plane, horizontal plane & End/Auxiliary Vertical Plane
Step 3: In a first angle Orthographic Projection, as shown, there are three standard views that can be produced namely: Front Elevation, Plan View and End Elevation.
Step 4: Taking an real-life 3D object, for example the L-Block as shown, the orthographic projection system allows us to generate 2-D views when looking at the object from a number of different positions.
Step 5: The projection lines show how the relevant views, depending on the viewing position, are generated onto each of the planar surfaces as well as showing the connected relationship between each of the views regarding shape and dimensions
Step 6: The 2-D representation shows how a first angle Orthographic projection is produced in 2D on an A3 page.
\
Vertical Plane
[VP]
Front - Elevation View
End/Auxiliary Vertical Plane
E/AVP
Side – End (Elevation) View
Horizontal Plane
[HP]
Top - Plan View
X
Y
When producing an Orthographic Projection we eliminate such space for both the Front Elevation and End View by positioning both views on the XY Line
FRONT ELEVATION
PLAN
END VIEW
X
Y
LEARNING TRACKER | 
JC KEY SKILLS | BEING CREATIVE, BEING LITERATE, BEING NUMERATE, COMMUNICATING & MANAGING MYSELF
KEY SKILL ELEMENTS | EXPLORING OPTIONS & ALTERNATIVES, EXPRESSING IDEAS CLEARLY & ACCURATELY, EXPRESSING IDEAS MATHEMATICALLY, USING LANGUAGE AND SETTING, INNOVATIVE THINKING & CRITIQUING SOLUTIONS
STATEMENTS OF LEARNING | SOL15 AND SOL21
LEARNING OUTCOMES | 1.1, 1.2, 1.3, 1.9, 1.12, 2.2, 2.3, 2.7, 2.8, 2.10 & 2.13
ACTION VERBS | INTERPRET, ILLUSTRATE, DEMONSTRATE, RECOGNISE, APPRECIATE, VISUALISE, DEVELOP & COMMUNICATE
KEY QUESTIONS | WHAT IS FIRST ANGLE ORTHOGRAPHIC PROJECTION?
 | HOW ARE VIEWS REPRESENTED ON EACH OF THE RESPECTIVE PLANAR SURFACES?
 | WHY DO WE NEED TO USE AN ORTHOGRAPHIC PROJECTION SYSTEM TO DESCRIBE AN OBJECT IN 2D?
3-2-1 STUDENT REFLECTION | 3 THINGS I LEARNED – WRITE IT ON THE PAGE
 | 2 THINGS I WANT TO KNOW MORE ABOUT – WRITE IT ON THE PAGE
 | 1 QUESTION I STILL HAVE – WRITE IT ON THE PAGE
B
A
C
Lets Draw!
Introduction To
First Angle
Orthographic Projection
2D Graphics & 3D Graphics
RESOURCE 18: FIRST ANGLE ORTHOGRAPIC PROJECTION SYSTEM
1.1, 1.2, 1.3, 1.9, 1.12, 2.2, 2.3, 2.7, 2.8, 2.10 & 2.13
Spatial Reasoning, Design Thinking, Communicating, Geometric Principles & Constructions